Assignement 2

Name:	Evan O'Keeffe
S#:	10324289

Question 1:

Part A:
1:Prime number(i.e only divisible by 1 and itself)
0:Non-Prime number

Part B:
Number	A	B	C	D	Y(Output)
0	0	0	0	0	0
1	0	0	0	1	0
2	0	0	1	0	1
3	0	0	1	1	1
4	0	1	0	0	0
5	0	1	0	1	1
6	0	1	1	0	0
7	0	1	1	1	1
8	1	0	0	0	0
9	1	0	0	1	0
10	1	0	1	0	0
11	1	0	1	1	1
12	1	1	0	0	0
13	1	1	0	1	1
14	1	1	1	0	0
15	1	1	1	1	0

Part C:
Expression : (¬A¬BC¬D)+(¬A¬BCD)+(¬AB¬CD)+(¬ABCD)+(A¬BCD)+(AB¬CD)

Part D:

Question 2:

Part A:
Majority is when there are 3/4 inputs on 1 i.e (0,1,1,1)
My decision on output signals that would be required

1:majority of bits are 1
0:majority of bits are not 1

Part B:

A	B	C	D	Y(output)
0	0	0	0	0
0	0	0	1	0
0	0	1	0	0
0	0	1	1	0
0	1	0	0	0
0	1	0	1	0
0	1	1	0	0
0	1	1	1	1
1	0	0	0	0
1	0	0	1	0
1	0	1	0	0
1	0	1	1	1
1	1	0	0	0
1	1	0	1	1
1	1	1	0	1
1	1	1	1	1

Part C:
Expression:	(¬abcd)+(a¬bcd)+(ab¬cd)+(abc¬d)+(abcd)

Part D:

Part E:

Boolean Simplification of Circuit
(¬abcd)+(a¬bcd)+(ab¬cd)+(abc¬d)+(abcd)

Steps:
1.={And distribution over OR} three times

a(¬bcd+b(c(d+¬d)+¬cd))+¬abcd

2.={complement.o on d+¬d}

a(¬bcd+b(c+¬cd))+¬abcd

3.={absorbption.0 c+¬cd}

a( ¬bcd + b(c+d) ) + ¬abcd

4.={And distribution over OR}

a¬bcd + abc + abd + ¬abcd

5.={And distribution over OR}

b( ac + ad + ¬acd ) + a¬bcd	{once}
b( d(a+¬ac) + ac ) + a¬bcd	{twice}

6.={absorbption.0 a+¬ac},{And distribution over OR} twice

abd + bcd + abc + a¬bcd

7.={And distribution over OR}

ad(b+¬bc) + bcd + abc

8.={absorbption.0 b+¬bc},{And distribution over OR}

(abd)+(abc)+(bcd)+(acd)

Part F:

Part G:
By inspection :

the number of pins from the simplified view to real circuits generally follow
the N-1 rule , i.e 4 input And gate is equivalent to 3 2-input And gates

By inspection :

Circuit 1:
4 NOT gates = 4*(0.7) = 2.8 G.E

4 input AND gates => 3 2-input ANDS gates => 3*5*(1.3) = 19.5
5 input OR gate => 4 2-input OR gates => 4*(1.3) = 5.2

Total G.E = 2.8+19.5+5.2 = 27.5 G.E

Circuit 2:
AND Gates:	4*(2)*(1.3) = 10.4
OR Gates :	3*(1.3) = 3.9
Not Gates :	None

Total Gate equivlance = 14.3 G.E

Difference of Gate equivalence :
Circuit 1 = 27.5	G.E
Circuit 2 = 14.3	G.E

Part H:

(14.3/27.5)*100 = 52 percent decrease in circuit area